## Slide 1: New understandings of inter-ELM pedestal turbulence, transport, and gradient behavior in the DIII-D tokamak
K. Barada1
In collaboration with
T. L. Rhodes1, S. R. Haskey2, R. Groebner3, A. Diallo2, S. Banerjee4, Z. Yan5, F. Laggner2, L. Zeng1, J. Chen1, and G. Wang1
1University of California, Los Angeles, CA, USA
2Princeton Plasma Physics Laboratory, Princeton, NJ, USA
3General Atomics, San Diego, CA, USA
4College of William and Mary, Williamsburg, VA, USA
5University of Wisconsin, Madison, WI, USA
This work was supported by the US Department of Energy under grants DE-FG02-08ER54984, DE-AC02-09CH11466, DE-FG02-08ER54999, DE-SC0019302 and DE-FC02-04ER54698.
Presented at the
28th IAEA Fusion Energy Conference
10th-15th May, 2021

## Slide 2: Main points/Highlights: New and unique measurements shed light on inter-ELM thermal transport
Clear evidence of inter-ELM ITG-scale and TEM-scale turbulence with drive and damping mechanisms
This measured multiscale turbulence is consistent with the inter-ELM evolution of the observed estimated heat fluxes
Note: Although ETG and MTM modes are thought/predicted to explain some of the Qe, in this work ETG-scale ñ are not measured and the identification of MTM like modes are not conclusive.

## Slide 3: Complete understanding of all transport mechanisms is necessary to improve prediction of pedestal evolution
Pedestal can remain close to the Peeling-Ballooning (P-B) stability boundary for a significant amount of inter-ELM period
EPED1 model had many successes in predicting saturated pedestal height and width
KBM driven transport constrains until P-B modes excite an ELM
Drift wave turbulence is shear suppressed
In this work we will show clear evidence of inter-ELM drift wave like turbulence that is not completely shear suppressed
Improved and validated models can impact pedestal thermal flux predictions for ITER and future fusion devices.
Saarelma et al, PPCF (2013)
1Snyder et al, NF (2011)

## Slide 4: Experiments are performed in Lower Single Null shape H-mode plasmas with low frequency type-I ELMs
Ip~1 MA, Bt~2.1 T, Power close to PL-H, PNBI~2.3 MW, ~5.1x1019/m3
Longer inter-ELM periods offer better statistics for ELM synchronized analysis
Height and widths of ne, Te, and Pe pedestal are estimated from tanh fits to Thomson measured profiles.
Pedestal gradients are calculated from measured heights and widths.

## Slide 5: Electron Pedestal Gradients remain nearly saturated for most of the inter-ELM period
Three distinct phases: Relaxation/crash, recovery, and near saturation
During gradient recovery: Height increases and width decreases.
In gradient saturation phase: Both height and width increase.
Gradients of pedestal density, temperature, and pressure stay saturated for nearly 75% of the inter-ELM period.

## Slide 6: Main ion heat flux is close to neoclassical (NC) and electron heat flux is anomalous in the nearly saturated phase
Power balance estimated Qi is closer to NC values calculated from experimental gradients whereas Qe is anomalous (at ~0.74)
NC ion heat flux contribution to total ion heat flux changes at different radii
Decreasing , difference between estimated and neoclassical Qi increases (Haskey et al, IAEA 2020)
E. Viezzer et al., Nucl. Fusion (2017)
ASDEX-U
DIII-D, this work

## Slide 7: ITG and TEM-scale ñ in the pedestal are measured by Doppler Backscattering (DBS) Diagnostics
Spatially, temporally, and wave number resolved ñ amplitude and its lab frame perpendicular velocity, are measured.
The 180º backscattered signal is Doppler shifted w.r.t incident wave (, ) and the intensity of the received signal is proportional to ñ.
Local ExB velocity shear is calculated from estimated at different probe radii
ITG-scale () ñ is measured near the foot of the pedestal whereas TEM-scale (-1.2) ñ is measured in the steep gradient region of the pedestal.
Notes: only L-mode

## Slide 8: ITG-Scale ñ near pedestal foot increases right after ELM and is subsequently suppressed until the next ELM
ITG scale ñ measured near foot of the pedestal increases just after ELM event
  Reduced progressively until next ELM but not completely suppressed
  Has temporal correlation with Divertor Dα emission intensity

## Slide 9: Suppression of ITG-scale turbulence correlates with ExB shear evolution and increase in pedestal
ExB shear near pedestal foot drops right after ELM crash and ITG scale ñ increases
Within few ms, local ExB shear increases and ITG-scale ñ is suppressed
increase is correlated with ITG-scale ñ suppression
*E. Viezzer et al., Nucl. Fusion (2017)

## Slide 10: TEM-scale ñDBS in the steep gradient region increases after a time delay from the ELM onset
Intermediate-k (TEM-scale) ñ propagating in electron diamagnetic direction (in the lab frame) with -1.2 measured in the steep gradient region
TEM-scale ñ increases after a time delay and the same delay has been observed in all steep gradient localized probed locations.
Notes: It is well known that anisotropy in turbulence eddies can generate Reynold’s stress which can create an electric field. This electric field with the Bt can generate flows. Though flow can be generated by ñ, it does not have any role in suppression. Flow can be suppressed then with ñ decrease. Why ñ decreases?, it can decrease by ExB shear. So we calculated ExB shear and plotted it against ñ.

## Slide 11: Steep gradient localized TEM ñ shows a critical behavior
In the steep gradient region, TEM scale ñ increases by nearly 3-5 times when a critical is recached in the inter-ELM period. = ~ 130 eV/cm.
TEM turbulence can be driven by but the threshold depends on background Ti/Te and [Casati et al, PoP (2008)]
A. Casati, et al, PoP (2008)

## Slide 12: TEM-scale ñ increases with supported by presence of increased background Ti/Te and
At critical , TEM-scale ñ increases supported by presence of increased background Ti/Te and
TEM-scale ñ is nearly saturated with nearly saturated and background Ti/Te and in the presence of higher ExB shear
This TEM-scale ñ has potential to drive electron heat transport and may contribute to the inferred anomalous Qe in the saturated phase

## Slide 13
Identification of the observed modes are attempted by varying and background Ti/Te and . This is done by ECH at ρ~0.5.

## Slide 14: With ECH, increases and decreases whereas does not change much
ECH at ⍴~0.5 added to beam heated discharge
Smaller and higher frequency ELMs replace larger low frequency ELMs
How different gradients change with electron heating?

## Slide 15: With ECH, decreases and increases but attains the same level as pure NBI case
With additional ECH:
Lower pedestal and higher
Pedestal is always higher than pure NBI case.
Pedestal increases nearly to same level as no ECH case before ELM crash.
Ti/Te decreases by a factor of 2 in the pedestal
How these above changes affect ITG-scale and TEM-scale ñ?

## Slide 16: At lower and lower , TEM-scale ñ decreases and ITG-scale ñ increases consistent with theoretical predictions
⍴~0.970
⍴~0.969
TEM ñ stabilization with ECH consistent with theoretical predictions1 of increased threshold for lower and lower
ITG-scale ñ increase is also consistent with this theory1 which suggests a lower threshold
Time averaged
ITG-scale ñ increases ~50%
TEM-scale ñ decreases ~66%
1A. Casati, et al, PoP (2008)

## Slide 17
Initial TGLF simulations in saturated phase suggest TEM-scale fluctuations are unstable in the steep gradient region
Linear TGLF simulations shows in the steep gradient region, the most unstable modes
have similar of TEM-scale ñ measured in experiment
propagating in electron diamagnetic drift direction in plasma frame
and near pedestal foot an unstable mode
propagating in ion diamagnetic drift direction at ρ~0.98
with ~0.2, close to the ITG-scale ñ observed in experiment
DBS measurement range in -ρ space in dashed rectangle

## Slide 18: Summary
New and unique measurements shed light on inter-ELM thermal transport by drift wave like turbulence
Evolution of ITG-scale turbulence regulated by ExB shear consistent with Qi decreasing from being anomalous to closer to NC
TEM-scale ñ increases at critical and can be responsible for anomalous Qe inferred from experiments
ITG and TEM-scale ñ evolutions are consistent with theoretical predictions of these being ITG and TEM instabilities respectively

## Slide 19: These observations can improve our pedestal evolution predictions by explaining some of the inter-ELM Qe and Qi
Thank you